## Slide 1: EDII quizzes
2023

## Slide 2
The electrostatic potential inside of a conductor
  is zero
  increases with distance from the center
  decreases with distance from the center
  is constant
The electrostatic potential in a universe that contains only conductors and vacuum can take maximum and minimum values
  only at infinity
  only at the boundaries between a conductor and vacuum
  only at the center of the conductors
  only midway between different conducting bodies

## Slide 3
The electrostatic energy of a system of charged conductors in vacuum
  is positive definite
  Can be positive or negative
  Is negative like the mechanical energy of planets
The quantities Cab with a not equal to b are called
  coefficients of electrostatic induction
  coefficients of capacity
  mutual capacitance

## Slide 4
Two dimensional problems of electrostatics are conveniently solved by
  the method of images
  the method of conformal mapping
  the method of inversion
The method of images tries to find fictitious point charges to make the mathematical surface of the conductor have
Group of answer choices
  zero potential
  constant potential
  a minimum potential

## Slide 5
Electrostatic forces on the surfaces of conductors
  are zero because the surface is an equipotential
  are always outwards from and normal to the conductor
  might not be normal if there are other charged conductors
  might be outward or inward depending on the sign of the charge
The net force on a conductor with zero net charge in a uniform external field
  is positive
  is zero
  depends on the distribution of positive and negative charges
  is negative

## Slide 6
The normal component of the electric field at the surface of a dielectric is proportional to
  the normal component of the polarization
  the polarization charge density
  the total surface charge density
  the extraneous surface charge density
The normal component of the electric induction at the surface of a dielectric is proportional to
  the extraneous surface charge density
  the total surface charge density
  the normal component of the polarization
  the polarization charge density

## Slide 7
The electric dipole moment of a dielectric body in an external electric field is NOT proportional to
  the polarizability
  the total electric field
  the volume of the body
  the electric field that would be present if the dielectric were absent
differentials of the internal energy and the free energy of a dielectric are related to each other by
  Legendre transform
  Laplace transform
  Laguerre transform
  L'Hopital transform

## Slide 8
At the interface between two conductors, which quantity is continuous?
  The normal component of the current density
  the normal component of the electric field
  the tangential component of the current density
  the tangential component of the electric induction
When the magnetic field changes sign, the symmetric part of the conductivity tensor
  must vanish
  changes sign
  is unchanged
  is complex conjugated

## Slide 9
The units of surface current density are
  charge/(time*area)
  charge/(time*volume)
  charge/(time*length)
  charge/time
At the boundary between two different media we must have
  normal component of H continuous
  normal component of B continuous
  tangential component of B continuous
  tangential component of M continuous

## Slide 10
In comparing magnetic and electric energies, the mathematical analogue of the electric potential is the
  charge density
  electric field
  vector potential
  current density
In comparing the electric and magnetic energies, the mathematical analogue of the vector potential is the
  current density
  scalar potential
  charge density
  magnetic field

## Slide 11
The magnetization of most bodies in an external magnetic field is small. In that case, the magnetic energy of the body equals the magnetic energy of the field produced by the given external currents in the volume of the body if the body was absent times 4p times
  the magnetic permeability
  the temperature
  the magnetic susceptibility
  the magnetization
In vacuum, the sign of the free energy of the magnetic field "script F tilda" is
  could have either sign
  negative
  positive

## Slide 12
Inductances are the coefficients of proportionality between the currents which produce the magnetic field and the
  magnetic fluxes
  circuit area
  magnetic field
  induced electric field
Self-inductance
  is proportional to the dimension of the conductor
  is independent of the shape of the conductor
  depends on the current in the conductor
  depends on the magnetic field the conductor is in.

## Slide 13
In the self inductance of a linear ciruit, the external part
  is comparable to the internal part
  Is negligible and be ignored
  makes the main contribution
  is identically zero due to time reversal symmetry
For a closed linear circuit, the self-inductance
  diverges logarithmically
  is constant through out space
  is zero because the current returns to the same point
  is finite

## Slide 14
The magnetic induction inside a superconductor is always...
  zero
  infinity
  indeterminate
  the same as the H-field
Any electric current that flows in a superconductor is
  a surface current
  a combination of surface and volume current
  a volume current
  infinte

## Slide 15
The quasistatic approximation applies to
  any kind of solid
  dielectrics
  conductors
  solids and viscous liquids
For the quasistatic approximation to be valid, the field frequency must be
  large compared to vibrational frequencies of ions in the lattice
  small compared to the reciprocal relaxation time of free electrons
  small compared to the orbital frequency of bound electrons
  large compared to the reciprocal mean free time of electrons

## Slide 16
Eddy currents are caused by
  thermal conduction
  electric fields of an incident electromagnetic wave
  induced electric fields from variable magnetic fields that penetrate into a conductor
  acceleration of the body
The magnetic field penetration depth in the quasistatic approximation
  proportional to inverse of frequency
  is proportional to frequency
  has frequency dependence that depends on whether the penetration depth is large or small
  is proportional to inverse square root of frequency

## Slide 17
In the expansion of the impedance in powers of frequency, the term linear in frequency is proportional to the circuit's
  self inductance
  resistance
  EMF
  current
The real part of the impedance...
  is positive
  is negative
  can be positive or negative
  is zero

## Slide 18
The frequency of undamped oscillations in an LCR circuit depends on
  L and C
  L and C and R
  R and C
  R and L
The capacitive part of the impedance varies as (w=frequency)
  wC
  L/wR
  1/wC
  w/LC

## Slide 19
Consider two actions. 1. A conductor moves within a constant magnetic field. 2 A conductor is stationary in a field that changes with time. Which effects can generate an emf.
  both
  neither
  the second
  the first
For a moving conductor in a static magnetic field, an emf appears only if
  the conductor crosses lines of magnetic field
  every point of the conductor moves along a line of force
  the conductor is doubly connected
  the conductor spins on its axis

## Slide 20
At frequencies much greater than 4 Pi sigma/epsilon, a material behaves as
  a crystal
  a conductor
  a dielectric
  a semimetal
In conductors at low frequencies, the displacement current is
  more important than conduction current
  approaching a constant limiting value
  diverging
  negligible

## Slide 21
At frequencies that approach the natural frequencies of motion that causes polarization, the electric induction is determined by the electric field
  at every previous instant
  at future instants
  not at all
  at the present moment only
At high frequencies, the distinction between dielectrics and conductors
  becomes more pronounced
  disappears
  remains unchanged
  No answer text provided.

## Slide 22
As frequency approaches infinity, the permittivity tends to
  unity
  infinity
  negative values
  zero
When frequency exceeds the natural frequencies of electrons in a conductor or dielectric, the electrons behave as though
  strongly interacting with the nuclei
  bound
  free
  strongly interacting with each other

## Slide 23
The rate of change of energy in unit volume of a body is
  div S
  S
  curl S
  S2
The total energy dissipated by a non-monochromatic pulse of electromagnetic energy a non-magnetic dispersive medium is proportional to
  the positive part of the permittivity spectrum
  the imaginary part of the permittivity
  the real part of the permeability
  the real part of the permittivity

## Slide 24
For dielectrics the function f(t), that tells how much the electric fields at earlier times a distance t into the past contribute to the induction at the present time, tends to zero as tau becomes large. For metals, the function that tends to zero is f minus a constant times....
  the conductivity
  the dissipated energy
  the permeability
  the permittivity
The complex permittivity is a function of the complex frequency. The permittivity is real on which axis of the complex frequency plane?
  positive real
  negative imaginary
  negative real
  positive imaginary

## Slide 25
The real part of the permittivity at a given frequency can be calculated from knowledge of
  the imaginary part of the permittivity at all frequencies
  the imaginary part of the permittivity at the same frequency
  The imaginary part of the permittivity at zero frequency
  the real part of the permittivity at zero frequency
The oscillator strength is proportional to
  the real part of the permittivity
  the imaginary part of the permittivity
  the inverse of the frequency
  the square root of the spring constant

## Slide 26
A wave for which k' and k" are not in the same direction is called
  a homogeneous plane wave
  an inhomogeneous plane wave
  an isotropic plane wave
  an anisotropic plane wave
The real part of of the permittivity e' is related to the real and imaginary parts of the complex index n + ik by
  e' = 2nk
  e' = k^2-n^2
  e‘ =2n/k
  e‘ =n^2 - k^2