## Slide 1: Equations of the Quasi-static Field
Section 58

## Slide 2
Until now, we considered only static electric and magnetic fields. We used
only to derive the magnetic energy.
2. Electrodynamics in matter depends strongly on the nature of the medium and on the frequency. Here we consider extended conductors in variable external magnetic fields at “low” frequencies (usually microwaves and below).

## Slide 3
The field at P due to the proximity of the conductor is the same in both cases, except that the magnitude and sign of the field at P in the latter case is changing monotonically as Exp[-i w t].
P has to be close enough to the conductor to avoid retardation effects: The field at P now is due to fields at the conductor now, not at earlier time.
Requires: distance to P << l.
3. First assumption: wavelength l ~ c/w >> body dimension l

## Slide 4
The equations of the static field should hold at the field point P, outside the conductor, where there is no charge current.
Let “l” be the dimension of the conductor

## Slide 5
4. Inside the conductor, the equations are different because the conduction currents are non-zero
with j = s E
We assume that Ohm’s law holds with the DC value of the conductivity:
This requires that the oscillation period of E >> electron response time t.
Otherwise E changes sign before macroscopic charge flow can build up.

## Slide 6
Requires: electron mean free path << characteristic length for changes in field.
Otherwise j at given point could be determined by E at distant points.
Local relations
5. The given quasistatic field equations in the conductor are local relations: The j at a given point depends only on the E at that point, and not at other points.

## Slide 7
6. The E-field appear inside the conductor is induced by the variable B-field
Any external slowly-varying E-field does not penetrate, but the B-field does.
Thus, dB/dt is the source for a macroscopic E-field inside.
small, but don’t discard it inside the conductor.
This is the internal E-field that drives the internal currents j

## Slide 8
Induced E-field distribution does not look like the external E0-field distribution

## Slide 9
If H is known, then
Gives j(r,t).
Then Ohm’s law
Gives E(r,t)
and
We can eliminate j and E to get a differential equation for H and B

## Slide 10
7. To eliminate B, we need to assume a relation between B and H. To simplify the equation, we need to assume medium is homogeneous.

## Slide 11
We get two equations for H, which suffice to find it everywhere at all times
Same as the heat conduction equation (Fourier’s equation):
Thermometric conductivity
z
H
Inside conductor
Outside conductor
Time rate of change of H(t) and curvature of H(z) are proportional at a given point

## Slide 12
8. Need boundary conditions on H to solve Fourier equation for H(z,t)
For a non-ferromagnetic medium, or ferromagnetic one at high frequency, m = 1.
Then B = H,
and boundary conditions become H1 = H2.
Since j is finite at the interface, see (30.2)

## Slide 13
9. Boundary conditions on normal component of E
En is usually zero at the outer boundary with dielectric (air).

## Slide 14
Boundary condition on Et for composite conductor.
E1t = E2t
This is a boundary condition for H that we can use to solve Fourier equation for H in the case that the conductor is piecewise homogeneous.
0
s1
s2
H
z
silver
copper
For a conductor with different parts of different s, Et is continuous at each interface.

## Slide 15
Suppose external H-field is suddenly removed.
The induced E and j don’t vanish immediately.
Neither does H in or around the conductor.
The decay of the field is determined by Fourier’s equation
Seek solutions of the form
This is an eigenvalue equation.
For a given conductor, solutions Hm(x,y,z) that satisfy the boundary conditions exist only for certain gm (real and positive).
{Hm(x,y,z)} = complete orthogonal set of eigenvectors.

## Slide 16
Let the initial field distribution

## Slide 17
l = dimension of the conductor
= largest dimension of the problem
Gives longest t, smallest g
High conductivity and large conductor give slow decay
The rate of decay is determined mainly by the smallest gm. Call it g1