## Slide 1: PtSi MWIR Camera SOP
2 Oct 2020

## Slide 2
All the parts in the silver brief case. Not shown is the laptop computer.

## Slide 3
1. Plug in the power supply

## Slide 4
2. Connect the camera
This block detaches

## Slide 5
Easycap USB connector to laptop computer. Use right USB port, not the one shown.
Use black cable
3. Connect to computer

## Slide 6
4. Turn power on.

## Slide 7
5. Turn Camera on. Takes 10 min to reach operating temperature

## Slide 8
Laptop computer. Linux. User “Pedro”, Password “3833626”
Program: Cheese
Preferences: AV to USB 2.0
Use WebCam button to capture an image
Image appears in album. To save to USB drive, right double click on image you want.

## Slide 9
Remove cap from camera
Choose Auto Span
4 ranges of integration time